## Slide 1: Expert Agent
Task 2.1 – Knowledge-assisted AI
IRT SystemX

## Slide 2: Outline
Context
Methodology
Original Contribution
Overview of code structure
Algorithm #1
Algorithm #2

## Slide 3: Context
Expert Agent is an RL agent where the exploration capability may be guided by expert knowledge.
The huge action space size in some critical infrastructure may cause some problems such as generalization, overfitting, instable and delayed convergence and exporation becoming intractable. The expert knowledge help the agent to be trained on effective and reduced action space while not avoiding the whole actions space exploration.
This implementation is specific to Power Grid domain and power grid assistant use case. In this use case, AI assistant supports human operators in decision-making and managing power grid congestion by suggesting remedial actions.
Definition
Motivation
Use cases

## Slide 4: Methodology
Main idea = Exploit the Expert Knowledge using ExpertOp4Grid package 1 to
  (1) focus the exploration phase of an RL agent on specific zones of a power grid
  (2) reduce the action space to most relevant ones and improve the scalability or RL agents
Use a gymenv enabling the access to original action space and states
Focus the exploration phase of the agent on a specific zone or reduce the action space based on expert knowledge
An RL agent explores the whole or reduced action space based on expert knowledge
The extended RL agent could explore and learn from expert knowledge for stability and traceability
Preliminary experiments on Power Grids, but could easily be extended to other doamins if the expert knowledge is available
Knowledge-assisted RL

## Slide 5: Schematic representation of the methods
Main idea = Exploit the Expert Knowledge to
  focus the exploration phase of an RL agent on specific zones of a power grid
  reduce the action space to most relevant ones and improve the scalability or RL agents
1
2

## Slide 6: Original contribution
Algorithm #1 | DeepQExpert
Short description: Focus the learning to the zones suggested by expert knowledge
State-of-the-art: Classical deep reinforcement learning algorithms 1 or expert system 2
Contribution: Exploitation of expert knowledge during the training of an RL agent
Implemented WP2 features: Knowledge-assisted RL
Algorithm #2 | ExpertAgent (better scalability)
Short description: Exploiting the reduced action-space obtained using expert knowledge as preprocessing
State-of-the-art: Classical deep reinforcement learning algorithms 1 or expert system 2
Contribution: Train the classical RL algorithms on reduced action space obtained using expert knowledge
Implemented WP2 features: Knowledge-assisted RL
1Rocchetta, Roberto, et al., A reinforcement learning framework for optimal operation and maintenance of power grids (2019)
2Marot, Antoine, et al., Expert system for topological remedial action discovery in smart grids (2018)

## Slide 7: Overview of repository structure
The provided repository includes a python package implementing two main expert agents
DeepQExpert
ExpertAgent
ExpertAgent
…
ExpertAgentHeuristic
ExpertAgentRL
…
…
utils
…
Python package
Method #1, focus the exploration based on expert suggested zones
Method #2, use an RL agent on reduced action space obtained using expert knowledge
Heuristic based approach
Learning-based approach
Utilities to extract action spaces using expert knowledge

## Slide 8: Authors
Authors | Institution
Milad Leyli-abadi | IRTSX (IRT SystemX)

## Slide 9: Algorithm #1

## Slide 10: Schematic representation of Algorithm #1
Main idea = Exploit the Expert Knowledge to
  focus the exploration phase of an RL agent on specific zones of a power grid
  reduce the action space to most relevant ones and improve the scalability or RL agents
    Heuristic-based
    RL-based
1
2

## Slide 11: Procedure
Harness Expert knowledge for an RL agent
ExpertOp4Grid framework
Extract expert knowledge
Implementation of the adapted DeepQ to exploit the expert knowledge in power grid use case
Experimentation and benchmark
Analysis of the impact of the expert knowledge (transparency + Explainability)
Use an existing work to exploit expert knowledge
Allows to identify the high impact zones for exploration
Extended DeepQ algrithm harnessing expert-suggested zones
Explanation
See presentation
T2.3 - explainability

## Slide 12: Algorithm
DeepQ Simple
DeepQ Expert

## Slide 13: Overview of code structure
DeepQ harnessing the expert knowledge
L2rpn_case14_sandbox
DeepQExpert
…
Python package
Trained DeepQ weights for 14 nodes environment
DeepQAgent.py
DeepQNN.py
deepQExpert.py
config.ini
train.py
evaluate.py
Base class including main functionalities
Neural Network (NN) implementation (tensorflow)
Expert Agent class including training loop
Configuration file used for expert knowledge (ExpertOp4Grid)
Script provided to train the agent
Script provided to evaluate the agent

## Slide 14: Grid representation
Environment = ai4realnet_small
# Lines = 20
# Substations = 14
# Generations = 6
# Loads = 11

## Slide 15: Inputs
Observation space include the following variables with a total of 197 values
Variable | Length | Variables | Length
day_of_week | 1 | actual_dispatch | 6
hour_of_day | 1 | target_dispatch | 6
minute_of_hour | 1 | topo_vect | 57
prod_p | 6 | line_status | 20
prod_v | 6 | time_before_cooldown_line | 20
load_p | 11 | time_before_cooldown_sub | 14
load_q | 11 | rho | 20
 |  | timestep_overflow | 20

## Slide 16: Inputs (for 36 nodes)
Observation space include the following variables with a total of 614 values
Variable | Length | Variables | Length
day_of_week | 1 | actual_dispatch | 22
hour_of_day | 1 | target_dispatch | 22
minute_of_hour | 1 | topo_vect | 177
prod_p | 22 | line_status | 59
prod_v | 22 | time_before_cooldown_line | 59
load_p | 37 | time_before_cooldown_sub | 36
load_q | 37 | rho | 59
 |  | timestep_overflow | 59

## Slide 17: Output data
A folder with saved models, hyperparameters, cumulative rewards and alive times steps, and action space used during the training of the model
A folder including the evaluation logs for each chronic selected during the evaluation and includes the following information
  Execution_time
  Rewards
  Other rewards (if there are any other optional rewards are computed in parallel)
  Actions
  Env_modifications
  Observations
  Oponnent attack

## Slide 18: Experiments
Mean Alive
178
0.01
DeepQ Simple
DeepQ Expert
Training loss
Mean Alive
230
0.008
Training loss

## Slide 19: Performance on test scenario
DeepQExpert
Number of episodes : 8
Max duration : 8000
Performance measured based on
  Agent’s alive time
  Reward

## Slide 20: Perspectives
Improve the agent hyperparameters using a fine-tuning algorithm

## Slide 21: Algorithm #2

## Slide 22: Schematic representation of the methods
Main idea = Exploit the Expert Knowledge to
  focus the exploration phase of an RL agent on specific zones of a power grid
  reduce the action space to most relevant ones and improve the scalability or RL agents
    Heuristic-based
    RL-based
1
2

## Slide 23: General Procedure
Harness Expert knowledge for an RL agent
Use ExpertOp4Grid framework
Extract expert knowledge
Using an approach to harness the expert knowledge
Experimentation and benchmark
Analysis of the impact of the expert knowledge (transparency + Explainability)
STEP 1
Reduce the action space
Extracting effective actions using expert
Heuristic-based
Option 2.A
STEP 2
Selecting an action
RL-based
Option 2.B
Explanation
See presentation
T2.3 - explainability

## Slide 24: Step 1. Reduce action space
ExpertOp4Grid package
https://github.com/marota/ExpertOp4Grid
# list to keep reduced action space
ExpertActions = []
# iterate over all the episodes
for episode in all_episodes:
# iterate over all the time stamps
for timestamp in len(episode):
# call ExpertOp4grid Package
topoActions, scores = call ExpertOp4Grid
# filter actions with high scores (3 & 4)
candidateActions = topoActions[scores>=3.]
# verify to not implicate new overloads
for action in candidateActions:
obs, reward, done = env.simulate(action)
# check no overload
if obs.rho.max() < 1.:
# append the action to the list
topoActions.append(action)
# store all the extracted actions
store(ExpertActions)
Action extraction pseudocode
Simulate and assess the remedial actions and attribute a score as:
4 - it solves all overloads,
3 - it solves only the overload of interest
2 - it partially solves the overload of interest
1 - it solves the overload of interest but worsen other overloads
0 - it fails to relieve even partially the overload

## Slide 25: Grid representation
Environment = ai4realnet_small
# Lines = 59
# Substations = 36
# Generations = 22
# Loads = 37

## Slide 26: Reduced action space
Extracting most effective actions using ExpertOp4Grid running on various scenarios
Reducing the original action space including only topological action set actions from ~ 30 000 to only 224 effective actions
Overload Graph
Identifying most effective actions

## Slide 27: Step 2. Option a) Use heuristic-based agent
Inspired by and extending the winning solution of L2RPN 2023 IDF challenge
Greedy search over reduced action space obtained using the expert knowledge
Use a set of well-known heuristics for power grid control
Reconnecting the disconnected lines
Return to the reference topology
Apply an existing convex optimization for continuous control (credit to LJN agent)
env, obs, reward # # Inputs : Get the environment, current observation and reward
action = env.action_space({}) # Initialize the action by doing nothing
reco_action = try_to_reconnect(obs, action, reward) # Try to reconnect
if reco_action is not None: # verify if there exists a potential reconenction action
_obs, _reward, _done = obs.simulate(action, time_step=1) # simulate the act
if not(done) & obs.rho.max() < 2.:
action += reco_action # add the reconnection to initial action if the overload less than 2
if obs.rho.max() > 0.99: # if an overload is observed
# try to recover the reference topology if possible
recover_act = try_to_recover_topo(obs, action, reward)
if recover_act is not None:
action += recover_act
else:
# retrieve the reduced action space obtained by the expert from step 1 (previous slide)
topo_act = search_expert_actions(reduced_action_space)
action += topo_act if topo_act is not None
_obs, _reward, _done = obs.simulate(topo_act, time_step=1)
if_obs.rho.max() > 0.9:
# Peform a convex optimization for continuous actions if no effective actions suggested yet
action = get_continuous_action_by_optimization(obs, action, reward)
elif obs.rho.max() < 0.9:
# try to recover the reference topology if possible whenever possible, even if no overload observed
recover_act = try_to_recover_topo(obs, action, reward)
if recover_act is not None:
action += recover_act

## Slide 28: Input data
Heuristic-based agent
Grid2op Environment (ai4realnet_small)
The path to reduced action space (obtained using expert knowledge)
The definition of overload thresholds
  Danger >= 0.99
  Safe = 0.9
Evaluation
Number of episodes for evaluation
Max iterations (time stamps) to evaluate per episode

## Slide 29: Output data
Evaluation logs
Proposed actions based on heuristic and expert knowledge
Diagram showing the performance of the agent

## Slide 30: Experiment
Tested on 15 episodes of environment
ai4realnet_small

## Slide 31: Step 2. Option b) Use RL-based agent
Train a Proximal Policy Optimization (PPO) algorithm on reduced action space obtained in step 1
Use a set of well-known heuristics for power grid control at inference time
Reconnecting disconnected lines
Return to the reference topology
Apply an existing convex optimization for continuous control (credit to LJN agent)
env, obs, reward # # Inputs : Get the environment, current observation and reward
action = env.action_space({}) # Initialize the action by doing nothing
reco_action = try_to_reconnect(obs, action, reward) # Try to reconnect
if reco_action is not None: # verify if there exists a potential reconenction action
_obs, _reward, _done = obs.simulate(action, time_step=1) # simulate the act
if not(done) & obs.rho.max() < 2.:
action += reco_action # add the reconnection to initial action if the overload less than 2
if obs.rho.max() > 0.99: # if an overload is observed
# try to recover the reference topology if possible
recover_act = try_to_recover_topo(obs, action, reward)
if recover_act is not None:
action += recover_act
else:
# search the best action over top_k prediction of ExpertAgent RL
topo_act = search(ExpertAgent_RL.top_k_predictions)
action += topo_act if topo_act is not None
_obs, _reward, _done = obs.simulate(topo_act, time_step=1)
if_obs.rho.max() > 0.9:
# Peform a convex optimization for continuous actions if no effective actions suggested yet
action = get_continuous_action_by_optimization(obs, action, reward)
elif obs.rho.max() < 0.9:
# try to recover the reference topology if possible whenever possible, even if no overload observed
recover_act = try_to_recover_topo(obs, action, reward)
if recover_act is not None:
action += recover_act

## Slide 32: Input data
RL-based agent
Grid2op Environment (ai4realnet_small) and its Gym counterpart
The path to the trained PPO model
The hyper-parameters of the PPO policy (MLP Policy)
Evaluation
Number of episodes for evaluation
Max iterations (time stamps) to evaluate per episode
Agent
Environment
Seed

## Slide 33: Output data
Evaluation logs
Proposed actions based on heuristic and expert knowledge
Diagram showing the performance of the agent
Tensorboard logs showing convergence informaiton and training losses

## Slide 34: Experiment
Tested on 15 episodes of environment
ai4realnet_small

## Slide 35: Perspectives
Extensive hyperparameter tuning of the RL model (PPO)
Integrate various variations of the environment (scenarios) during the training

## Slide 36: Link to the repository
AI4REALNET/T2.1_deep_expert: Expert Agent exploiting the expert knowledge during the training